## Slide 1: Userspace squash filesystem for launching Linux containers on hpc systems
by Ronald shane goff
LA-UR-19-24149

## Slide 2: Software in high performance computing
Carefully administered and managed – very stable long term
Only some versions of some things are installed
  Might be missing an older or newer version you need
New software can be requested
  Without great enough need the burden of support is too high
LA-UR-11-1111

## Slide 3: Building your own software
You can build your own software for most things
Can be a hassle to debug and repeat this
Usually no internet access
Have to rebuild every time on a new platform
LA-UR-11-1111

## Slide 4: The quest for software isolation
Many have numerous specific dependencies that are not supported
Building software can be difficult
If you change platforms, you have to build everything again
If you change software versions you have to build again
Must get the software to the compute center without the internet
LA-UR-11-1111

## Slide 5: Virtual machines for isolation
Uses an entire guest operating system
Separate user libraries and binaries
Separate kernel from the host
Uses a hypervisor to give guest access to host hardware
Almost entirely separate from the host
Usually no access to special hardware used in HPC
Keeps host kernel safe from blunders
LA-UR-11-1111

## Slide 6: Linux containers
Separates user binaries and libraries from the host
Shares operating system kernel with the host
  Can directly access special hardware
  Smaller than virtual machines
  More risk to the host
Uses Linux name spaces to separate resources instead of a hypervisor
Lower overhead not having to start an entire operating system
LA-UR-11-1111

## Slide 7: Containers are closer to bare metal
LA-UR-11-1111

## Slide 8: Why containers
Fast
Lightweight
Unfettered internet access at build time
Reproducible
Portable
LA-UR-11-1111

## Slide 9: We must also ask why not containers
User defined software stacks introduce new attack vectors
Some container run time tools require root
Containers can use more system memory than bare metal
LA-UR-11-1111

## Slide 10: Unprivileged workflow
Containers by design do not need root to execute
Some tools provide services to users that need root
  Uses a root-level process to start user containers
  Parent process also handles root-level things it needs to work
  Concerning to most cluster admins, can expose root access to users
  Extra services mean extra effort to support
LA-UR-11-1111

## Slide 11: Running containers in hpc
Some tools require root for running containers
  Docker swarm
  Singularity
  Shifter
Some do not
  Charliecloud
LA-UR-11-1111

## Slide 12: Using Charliecloud
To use containers on HPC resources the container must be made available to all compute nodes within the cluster in some way
Charliecloud only requires a directory tree resembling a Linux filesystem tree
Docker containers are exported to a compressed tar file, then unpacked to memory on each node
LA-UR-11-1111

## Slide 13: Other ways to distribute containers
You can run the container from a networked filesystem
  No need to distribute containers manually
  Slower execution time of containers, but less preparation time
  Only copies necessary files instead of the whole container, using less memory
LA-UR-11-1111

## Slide 14: Enter The squash filesystem (squashfs)
Compressed read only filesystem
Already used by some container tools, like Shifter
  Uses a kernel mounted squash filesystem to make container images available over a network filesystem
  The reason Shifter requires root-level access
Proven to be fast and efficient for containers in HPC
Hosted on an existing network filesystem like Lustre
LA-UR-11-1111

## Slide 15: Do we need root for squashfs?
Kernel mounted squashfs is fast and great, but needs root
Existing tools can make use of the squashfs without root via Filesystems in userspace (FUSE)
FUSE is generally considered to add overhead
LA-UR-11-1111

## Slide 16: A little about lustre
Parallel filesystem that uses object storage
Separates file data and metadata
  Uses servers to make bits available
  Metadata server
  Metadata targets
  Object Storage server
  Object Storage targets
LA-UR-11-1111

## Slide 17: Lustre and squashfs
Lustre doesn’t deal well with small file transactions, due to having separate metadata
Containers can have many small file transactions, as most binaries and libraries aren’t very large
Squashfs contains and compresses metadata
  Keeps everything bundled together
  Presented as a single file to Lustre, avoiding lots of metadata transactions
LA-UR-11-1111

## Slide 18: FUSE
FUSE allows users to mount filesystems without root
User level processes communicate with kernel driver to do work
  Users can ONLY start user level processes, kernel driver is separate and handles root stuff
Low-level FUSE API
  Faster, harder to develop
High-level FUSE API
  Wraps around low-level API, adds more overhead converting paths to inodes
LA-UR-11-1111

## Slide 19: Objectives
Find out what amount of overhead is added to squashfs through FUSE
Explore options to minimize overhead, and optimize the squashfs on Lustre
  Containers don’t fit well in Lustre best practices
  There are options for squashfs block size we can adjust
  There are Lustre options we can adjust for squashfs
LA-UR-11-1111

## Slide 20: The pynamic benchmark
Developed at Lawrence Livermore National Laboratory
Designed to test a systems ability to handle the Dynamic Linking and Loading requirements of Python-based scientific application
Creates a number of arbitrary library files
Reports timings for loading these files
LA-UR-11-1111

## Slide 21: Method
Factors | Levels
Node Count | 1,128,512,1024
Mount Method | kernel, squashfuse, squashfuse_ll
Squashfs Block size | 128Kib, 1MiB
Lustre Stripe Size | 64KiB, 1MiB
Lustre Stripe Pattern | 1 OST, 2 OSTs, 32 OSTs
LA-UR-11-1111

## Slide 22: misc
Some experiment iterations were run on Network Filesystem instead of Lustre, for science.
Not all things will resemble an HPC workflow
  A recursive grep will be run on the squashfs which will walk the whole filesystem to test limits. Even though containers won’t do such a thing, someone will.
LA-UR-11-1111

## Slide 23: Results
Kernel mounted squashfs is king
  Doesn’t care about any attempts or lack of attempts at optimizing
  Fastest in all configurations, very stable
High-level FUSE API was slowest
  Shows more impact regarding optimization
Low-level FUSE API was in the middle
  Shows similar but less obvious benefits from optimizations
LA-UR-11-1111

## Slide 24: Lustre striping matters
Default squashfs block size, Lustre stripe size, and stripe count
Increasing stripe pattern from one stripe, to two greatly improves performance as scale increases
LA-UR-11-1111

## Slide 25: Squashfs block size
Smaller squashfs block size is faster than a larger one
Squashfs block size can be smaller than the default 128KiB, but was not tested
LA-UR-11-1111

## Slide 26: Lustre stripe size
Less impactful than the other factors
The curve for the High-level FUSE API is slightly flatter with a smaller stripe size compared to larger
Lustre stripe sizes larger than the default were not tested
LA-UR-11-1111

## Slide 27: FUSE overhead
High-level API has more overhead
Low-level API is very close in the reported benchmarks to a kernel mounted squashfs
When optimized performance is maintained as scale increases
FUSE overhead scales very well and is manageable
LA-UR-11-1111

## Slide 28: Misc tests
Tests on NFS were short lived, at 64 nodes Pynamic took 10 minutes
Recursive grep had some quirks
  Using high-level FUSE API recursive grep was quite slow, but finished even at 256 nodes
  Took 370 seconds at 128 nodes
  Worked at 256 nodes, gave questionable output after that
  The low-level API was fantastically faster, but at higher node counts hangs with no error
  Took 100 seconds at 128 nodes
  Failed at more than 128 nodes
LA-UR-11-1111

## Slide 29: Caveats
FUSE has a default maximum request size of 128KiB
  Could explain why larger block sizes appear to hurt performance, instead of help
There were no attempts to optimize FUSE
Never figured out why the low-level API hangs on recursive grep
There was no competition for resources through the experiment
  This will never happen in the real world
Did not use enough different block and stripe sizes
LA-UR-11-1111

## Slide 30: Conclusions
Using default squashfs block size and Lustre stripe size is best and easiest
Striping across OSTs becomes more important at scale
FUSE overhead is rather small, and appears to stay that way with the low-level API
Kernel mounted squashfs is fastest, but less secure due to root access
LA-UR-11-1111

## Slide 31: Future work
Testing should be done across a larger scale
More block and stripe sizes should be tested
FUSE can possibly be optimized
  New versions support new features
  Maximum request size can be increased
Squashfuse has not been updated in 8 years, there may be improvements that have made their way to the kernel code
LA-UR-11-1111

## Slide 32: Question time
LA-UR-11-1111